v9.1 07/25/84

		  The SD Super Directory Program

     This documentation file concerns SD-91.ASM.  This is a signifi-
cant upgrade of the standard "super-directory" program that most RCP/M
systems are now using as their "DIR" executor.

     The newest features deal with video display format.  Several new
equates have been added to allow maximum flexibility to the user or
SYSOP.  A description of these equates follows:
    A new feature has been added that does away with the need for several
versions of SDxx.  SD-91 allows the inclusion of a 4, 6, or 8 on the
command line which relates to 40, 64 & 80 column display. (2, 3, or 4
filenames per line.)  The default value is that stored in NPL and LPS if
MAXCL is NO, and the value at MAXCL and LPS1,2 or 3 if MAXCL is YES.
    MAXCL  This equate, if YES, enables RCP/M operators to store the value
of 2, 3, or 4 at the location defined by MAXC.  Just have your signon or
RBBS program ask for or assign a value for NPL (names per line) and store
it at the location MAXC.  The suggested addresses for MAXC are, 3BH if using
3EH for the wheeel byte location or 3EH if using 3BH for the wheel byte.
No more need to keep several versions of SD online. ie DIR40, DIR64.
    The following equates are the values for the number of lines per
screen (LPS) to be changed as needed when MAXCL = YES.
  LPS1  This is the number of lines per screen if NPL = 3. (64 col option)
  LPS2  This is the number of lines per screen if  NPL < 3. (40 col option)
These additional equates allow one to specify the number of lines that will
be displayed for each of the optional formats (4 & 6).  This would allow
one to set up SD for optional remote use with a TRS-80 Mod 100 (for example)
by setting LPS2 to a value of 8.

Here are some command line examples:

   If MAXCL = yes
SD <cr>
   Will display all files on current drive using the value stored at MAXC to
determine the number of filenames per line.

SD $6 <cr>
    Will display all files on the current drive and display files in the 64
column mode (3 filenames per line).  It will also store a 3 at the memory
location defined by MAXC for subsequent use by SD or any other utility
that uses the variable filenames per line function.

   If MAXCL = NO
SD <cr>
   Will display all files on the current drive using the value defined by
the NPL equate.

SD $4 <cr>
    Will display all files on the current drive and display files in the 40
column mode (2 filesnames per line).  It will revert to the mode defined by
NPL on subsequent uses of SD.

    KTHREE  This equate allows control over the number of columns used
in the display of file sizes.  If KTHREE = YES then only three digits
with be used, limiting proper display of file sizes to 999k or less.
If KTHREE = NO then SD will use five digits as it has as of SD-89,
allowing files as large a 64,535k to be displayed.  The advantage of
KTHREE = YES is that you may now use a fence charcter even in the four
file display mode.  This makes the display more readable. Note: As of
SD-91, KTHREE only changes the display of individual file sizes and
totals are not affected.
     PDRI & PRUS  These equates allow (if YES) or disallow (if NO) the
printing of the drive and/or user numbers at the front of each file
display line.  These affect only the video format and all printer formats
still report the drive (and user if REPUSR = YES) numbers.  This allows
the display of the user number without the drive spec if this format is
needed.  A good example would be a 40 column format used on a RBBS which
makes use of a large number of user areas.
     PRLIBD  If this equate is set 'NO' & PRDI and PRUS are 'YES',
SD will suppress the display of drive/user numbers on LBR file display
lines.  One may wish to use this format if PRBRDR = YES.
     PRBRDR  allows the printing of a quasi-border around the left side
of library file member lines if set 'YES'.  This makes for a much more
readable format when displaying a large number of LBR files.

     The most significant improvement is the support of the DU: form for
drive-spec, similar to that used by ZCPR2 and its various utilities.
This is concurrent with the $U option.	The filename of the file for the
$F option has been altered to SD.DIR, as it was originally.  Other op-
tions such as multi-drive search remain as before.  Now, in place of the
$U option, you may specify the Drive/User with the filename, such as:
SD A1:*.*, SD 1:*.*, SD B:FN.FT, SD B4:FN.FT $AD, etc.	You may still
use the $U option if desired, although it seems the DU: form is a much
easier and more logical method.  File lengths over four megabytes are
read correctly.

     Files  may be  shown in vertical or horizontal listings, although
this must be set when the program is assembled for a particular system.
The distribution copy is set for vertical alphabetization since most
non-RCPM users will likely prefer this presentation.  (SYSOPs will need
to set a number of equates and reassemble the file in any event.)

     SD-91 has support for .LBR files, (an 'L' option to list their
member files); and support for the NZCPR/ZCPR2 "WHEEL" byte option.
(SD-91.COM is not set up for ZCPR2 use.)  Size of library
 member files  are shown in 'k'.

     The basic operation of SD is as in previous releases.  You merely
type "SD", followed by an optional ambiguous or nonambiguous filename
(as you would with the CCP directory command).	Omitting the filename
(i.e., "SD <cr>"), will be interpreted as "SD *.*".  Similarly, "SD A:"
would imply "SD A:*.*" and "SD B:" would  imply "SD B:*.*".

     In addition to the filename option, up to 11 command line options
may be specified.   Option fields are preceded by a single dollar sign
as with most Digital Research programs such as MAC, and may be essen-
tially free-form in format.  Example:  SD B:$ADnU0fpS.	Spaces within
the option field are insignificant i.e., "$ SADN U0FP" is equivalent to
"$  S A D N  U0  F P").  The only exception concerns the "USER" option
which will be explained later.

     Users should also be aware of two restrictions on the command line
format.  SD scans the entire command line for a dollar sign preceded by
at least 1 blank to delimit the beginning of the option field.	Forthis
reason, invoking SD with a command line such as:  "SD $ $AR" is illegal,
since SD will consider the first dollar sign to be the option field de-
limiter.  If you need to specify a filename whose first  character is a
dollar sign precede it with a drive code as in "SD A:$ $AR".  In this
instance, SD will consider the first dollar sign insignificant as it is
not preceded by a blank.

     Starting with SD-75 there is an assembly time option which, if set,
allows the use of options without requiring the filename to be preceded
with a drive code so long as you wish to look on the default drive.

     You give up the ability to specifically search for a filename whose
name begins with a '$'.  However, such files will be listed, along with
others, if the command line "SD $CU3" (or any other options) were speci-
fied.  The "COM" file is configured with this option set.   Setting the
option to 'NO' and reassembling will cause operation to revert to that
of previous versions (see paragraph above).

     The second restriction is that command line options may be specified
once and only once per invocation.   That is, "SD A:$SDS" would be il-
legal since the 'S' option is specified twice.  This shortcoming is due
to the fact that options can be made into defaults at assembly time.
Note that if an option is made default, with zero as option flag, it
cannot be specified without generation an error message.  The eleven re-
cognized options:

  "S" - system option:	System files will be included in the
	output	rather than being suppressed.

  "F" - file  option:  The directory output  will be echoed to
	a disk file named "SD.DIR" on the DEFAULT drive.
	If this name already exists then the directory output
	will be APPENDED to the end of the file.  "SD.DIR"
	will otherwise start as a new file.  The append fea-
	ture allows you to build up one massive file on the de-
	fault drive containing the directories of all of your
	disks, without having to concantenate a swarm of indi-
	vidual directory  files.  If you plan to use this fea-
	ture often,it will be simpler for you to have a dedi-
	cated version  on  your  MAST.CAT disk with  AUTOR set
	'YES'.  The advantage of this is that you can work thru
	a pile of disks without having to CTL-C or specify the
	'R' option every time you SD a new disk.  Failing to do
	this will result in the allocation  vector being inval-
	id, and FREE size will be wrong.

  "U" - user option:  Allows the specification of the user num-
	ber for the directory of the form "Uxx" where the user
	# is greater than 0, but not greater than a specified
	value not to exceed 15.  The user option specification
	will be illegal if the user # is out of range, omitted,
	or if 'U' is specified on a pre-CP/M 2 system.  Since
	the user option requires a parameter (i.e., the user
	number), the user number must immediately follow the 'U'
	option on the command field.  That is, "U1" is legal,
	but "U	1" is not.  In this respect, the 'U' option
	differs from the other options in that embedded spaces
	ARE significant.

  "A" - all users:  Causes SD to display directories of all
	user areas starting at the user area specified in the
	'U' option or, if the 'U' option is omitted, user area
	0 and continuing up through the MAXUSR value from the
	LODRV-HIDRV table.  (If ZPR2/WHLUSR=TRUE and the WHEEL
	byte set, 0-MXZUSR.)

  "L" - LBR list option:  Allows for listing of ".LBR" file
	members.  ".LBR" file members are shown followed by
	their length  in 'k'.  The total length of the entire
	library is also shown.

  "V" - If included, SD version number is displayed.

  "C" - If  included, clear  screen  performed before directory
	information is displayed.

  "N" - no page  option:  Unconditionally disables the page
	pause option.  Useful when running SD in the 'F' and/or
	'A' modes when you don't want the page prompt slowing
	you  down.  SD-91 will not put the page-pause prompt
	into the output file or to printer if either enabled.

  "P" - printer option:  Forces all console output to be echoed
	to the CP/M list device, with the most significant bit
	set to 0.

  "D" - all disk option:  Allows SD to search all disk drives
	on-line starting with the disk drive specified or im-
	plied with the command line filename.  For example,
	"SD B:$D" will result in SD searching all drives begin-
	ning with drive B.  "SD $D" will result in SD searching
	all drives automatically beginning with the A drive,
	regardless what drive you started on.

  "R" - Reset disk system:  A disk system reset is done before
	directory information is accumulated.

  "4, 6, or 8" - Filenames per line option: These will allow
        the user to specify the number of filesnames per line
        to be used in the display.  The format used relates to
        40, 64, & 80 column display which is 2, 3, & 4 lines
        per line respectivly.  If MAXCL = YES, the specified
        value is stored in the memory location defined by MAXC.
        If MAXCL = NO then SD reverts back to the value defined
        by NPL after displaying the optional format.  If MAXCL
        = YES and WHLCL = YES then SD will not allow the use of
        these a command line options and will use the value stored
        at MAXC for display.

     If an unrecognized option (or illegal user option specification) is
detected, then the command line will be played back to the console up to
the point where the error was detected.  However, if the REPERR option
is disabled, then SD will keep its mouth shut and ignore everything on
the command line past the illegal field.  In this situation, an illegal-
ly specified user number would default back to the current user number.
The option of DISABLING error reporting was included primarily for sys-
tems with hidden doors and secret passageways.	Shooting off rockets and
clanging bells everytime a twit starts "experimenting" just calls atten-
tion to the fact that there really IS something behind that hollow-
sounding  wall after all.

     As an added convenience, it is possible to "hard-wire" some or all
of the command line options.  For example, if you want SD to ALWAYS list
system files, you can do that.	For details, see the comments preceding
the option field lookup table in the assembler source file.

     Finally, if the all-disk and/or all-user options are enabled, it may
be  desirable to restrict searches.  To facilitate this, a table is in-
cluded in SD (beginning at label "LODRV" and continuing through "HIDRV").
The table consists of a single byte for each drive to be searched begin-
ning with 'A'.  Each byte may be in the range of 0-15 mod 15 and defines
the highest user number that SD will search for that particular drive.
The highest drive number to search is defined by the length of the table.
If four DBs are present between LODRV and HIDRV, then drives A-D can be
searched.  The source file includes the LODRV-HIDRV table in its maximum
configuration for 16 drives.  However, delete DBs referencing drives that
aren't available on your system.  Although SD will intercept attempts to
search non-existant drives, there really isn't any point in allowing SD
to always search drive C when you only have 2 logical drives; and de-
pending on how your BIOS is constructed and how long it monkeys around
before advising the BDOS of the select error, it could save some time.

     You don't really have to be running NZCPR or ZCPR2 to use the WHEEL,
MAXUSER, MAXDRIVE, or MAXCL byte features, just have your signon or RBBS
program assign and store the correct values in the proper locations to
enable these features, or add code to BYE-xx to provide the correct values
when a remote user logs on. (before entering CP/M).


; 04/17/84  Added TIMEON equate and TIME routine to calculate the time a
;   v8.2    user has been on and if STATUS is non-zero that delta time
;	    is compared to MAXMIN to see if user will exceed his total time
;	    limit.  If he does, the user is informed and logged off.
;	    This routine is similiar to XMODEM except QUITE set to YES will
;	    not report  "Time on system is xx minutes" but still checks
;	    MAXMIN.  If xx is => MAXMIN the user is told not to
;	    call back for 24 hours and automatically logged off.  If STATUS
;	    is non-zero, the "Time on system" message is displayed but
;	    no comparison to MAXMIN is made.
;
;	    The SYSOP must add code to the beginning of TIME which will
;	    read his realtime clock and store BINARY values of the cur-
;	    rent hour (0-23) and the current minute (0-59) in locations
;	    pointed at by CHOUR and CMIN.  The SYSOP must also code his
;	    BBS entry program (or BYE) to store the BINARY hour and min-
;	    utes of the user's logon time in LHOUR and LMIN.  The BBS
;	    (or BYE) software should also determine if the user has
;	    special privledges (such as SYSOPs, frequent uploaders etc.)
;	    and store FF (or non-zero) in the byte pointed at by STATUS.
;	    Store a 0 in STATUS for normal users.
;
;	      If TIMEON is YES, MAXMIN should be set to
;	    60.	 TIMEON uses 5 bytes in page one memory not used by CP/M
;	    (similiar to WHEEL and MAXDRIV).  They are:
;
;		CHOUR	EQU	043H	;for basic
;		CMIN	EQU	044H	;programmers the decimal to poke
;		LHOUR	EQU	050H	;is 80
;		LMIN	EQU	051H	;81
;		STATUS	EQU	053H	;and 83
;
;	    Be sure to store binary (not ASCII) in these locations.
;					- Wayne Masters


			- Written by Kim Levitt
			- Updated by Irv Hoff
                        - Further updates by Dennis Vallianos
			- Updated for SD-91   John Ray