Subject: Re: Manuals or Jumper Information needed

Date: 17 Aug 2004 18:36:14 -0500

From: r dot stek at snet dot net

Newsgroups: comp.os.cpm

References: <sssUc.23161$cT6.19307@fe2.columbus.rr.com>

Barry -

For the NorthStar 32k board -

'To configure for a continuous 32k byte region... four adjacent

switches should be ON (right side depressed) and the other four should

be OFF, according to the following table:

Address region        Switches on

0000-7fff                 0,2,4,6 (1st thru 4th)

2000-9fff                 2,4,5,8 (2nd thru 5th)

4000-bfff                 4,6,8,A (3rd thru 6th)

6000-dfff                 6,8,A,C (4th thru 7th)

8000-ffff                  8,A,C,E (5th thru 8th)

Certain groups of non-adjacent 8k address regions starting on 8k

boundaries can be selected if, using the following table, at most one

switch is ON from each column:

0  2  4  6

8  A  C  E

To use less than the entire board: 24k, 16k, 8k or 0k board results in

having 3, 2, 1 or 9 switches ON respectively.

Bob