Switch setting for the Cromemco 64KZ memory card.  Note, this is a different board from the 64KZ II.

SW1 
OFF / ON 
--------------------------------- 
1. DMA A = IN / OUT 
2. OVERRIDE A = DISABLED / ENABLED 
3. RESET A = OUT / IN 
4. DMA B = IN / OUT 
5. OVERRIDE B = DISABLED / ENABLED 
6. RESET B = OUT / IN 
7. A15 B = 0 / 1 
8. A15 A = 0 / 1 

SW2 - BLOCK A 
OFF / ON 
--------------------------------- 
1. BANK 0 = OUT / IN 
2. BANK 1 = OUT / IN 
3. BANK 2 = OUT / IN 
4. BANK 3 = OUT / IN 
5. BANK 4 = OUT / IN 
6. BANK 5 = OUT / IN 
7. BANK 6 = OUT / IN 
8. BANK 7 = OUT / IN 

SW2 - BLOCK B 
OFF / ON 
--------------------------------- 
1. BANK 0 = OUT / IN 
2. BANK 1 = OUT / IN 
3. BANK 2 = OUT / IN 
4. BANK 3 = OUT / IN 
5. BANK 4 = OUT / IN 
6. BANK 5 = OUT / IN 
7. BANK 6 = OUT / IN 
8. BANK 7 = OUT / IN