<!DOCTYPE HTML PUBLIC "-//W3C//DTD HTML 4.0 Transitional//EN"><!-- saved from url=(0102)http://www.hartetechnologies.com/manuals/Cromemco/Bytesaver%20Prom%20Burner%20Software/BYTESAVR_14.ASM -->

;----------------------------------------------------

;

;BYTESAVER EPROM PROGRAMMER CONTROL PROGRAM

;

;VERSION 1.4 - 10 SEP 77

;

;

;JEFFREY W. SHOOK

;P. O. BOX 185

;ROCKY POINT, NEW YORK 11778

;

;MODIFIED BY:

;

;BARRY A. WATZMAN, CDP

;2330 MILLENNIUM LN.

;RESTON, VA. 22091

;-----------------------------------------------------

;

;SYMBOL DEFINITIONS

;

BDOS	EQU	5		;CP/M BDOS ENTRY POINT

RCON	EQU	1

WCONB	EQU	9

CR	EQU	0DH		;ASCII CARRIAGE RETURN

LF	EQU	0AH		;ASCII LINE FEED

STATL	EQU	0FFH		;IMSAI CONSOLE STATUS LED'S

BYTSAV	EQU	0E000H		;BYTESAVER START ADDRESS

BEGDAT	EQU	1000H		;START OF DATA FOR EPROMS

NPASS	EQU	255		;NUMBER OF PROGRAMMING PASSES

;THIS VALUE FOR BYTESAVER WITH

;1.0 MSEC. PROGRAM PULSE

;

;MAIN PROGRAM CODE

;

ORG	100H		;CP/M STARTS EXECUTION HERE

;

;INITIALIZATION

;

LXI	SP,STACK

MVI	A,0		;CLEAR CONSOLE STATUS LED'S

OUT	STATL

;

;PRINT SIGNON MESSAGE & GET FUNCTION

;

LXI	D,SGNMSG	;SIGN-ON MESSAGE

CALL	PRTMSG

GTFUNC:	LXI	D,FUNCMSG	;POINT TO FUNCTION MESSAGE

CALL	PRTMSG

GTFNC1:	CALL	INCH

CPI	'X'

JZ	GOCPM

CPI	'D'

JZ	DDT		;RETURN TO DDT VIA RST 7

CPI	'C'

JZ	GDANS		;VALID ANSWER

CPI	'P'

JZ	GDANS		;VALID ANSWER

CPI	'E'

JZ	GDANS		;VALID ANSWER

LXI	D,WHATMSG

CALL	PRTMSG		;TELL USER ANSWER'S INVALID

JMP	GTFNC1		;GET FUNCTION AGAIN

GDANS:	STA	FUNCT		;SAVE REQUESTED FUNCTION

CALL	RANGE		;GET EPROM ADDRESS RANGE

CALL	ERASED		;CHECK IF PROMS ERASED

CALL	PROGRM		;BURN IN EPROMS

CALL	COMPAR		;CHECK IF TRANSFER CORRECT

JMP	GTFUNC		;DO IT ALL AGAIN

;

;RETURN TO DDT VIA RST 7

;

DDT:	RST	7

;

;RETURN TO CP/M

;

GOCPM:	JMP	0		;REBOOT CP/M

;

;THIS SUBROUTINE GETS THE EPROM NUMBERS (0-7) TO BE

;PROGRAMMED/VERIFIED AND CONVERTS THEM TO ADDRESSES

;

RANGE:	LXI	D,RNGMSG1

CALL	PRTMSG

CALL	GTPROM

JNC	GTBEG

LXI	D,PRMMSG

CALL	PRTMSG

JMP	RANGE

GTBEG:	SHLD	BEGPRM

LXI	D,RNGMSG2

CALL	PRTMSG

CALL	GTPROM

JNC	GTEND

LXI	D,PRMMSG

CALL	PRTMSG

JMP	RANGE

GTEND:	LXI	D,256*4

DAD	D

SHLD	ENDPRM

LDA	ENDPRM+1

LXI	H,BEGPRM+1

CMP	M

JZ	BAD

RNC

BAD:	ORA	A

RZ

LXI	D,PRMMSG

CALL	PRTMSG

JMP	RANGE

;

;THIS ROUTINE GETS A SINGLE PROM POSITION AND CONVERTS

;IT TO A STARTING ADDRESS

;

GTPROM:	CALL	INCH

SUI	'0'

RC

CPI	8

JC	GTPM1

CMC

RET

GTPM1:	MVI	L,0

MOV	H,A

DAD	H

DAD	H

LXI	D,BYTSAV

DAD	D

XRA	A		;CLEAR CARRY

RET

;

;ROUTINE TO CHECK IF PROMS ERASED

;

ERASED:	LDA	FUNCT

CPI	'C'

RZ

LHLD	BEGPRM

LXI	D,ERMSG

ERASE1:	MOV	A,M

CPI	0FFH

JNZ	ERASE2

INX	H

LDA	ENDPRM+1

CMP	H

JNZ	ERASE1

JMP	PRTMSG

ERASE2:	LXI	D,NERMSG

JMP	PRTMSG

;

;ROUTINE TO ACTUALLY PROGRAM THE PROMS

;

PROGRM:	LDA	FUNCT

CPI	'P'

RNZ

LXI	D,PWRMSG

CALL	PRTMSG

CALL	INCH

CPI	CR

JNZ	PROGRM

LXI	D,PGMMSG

CALL	PRTMSG

LXI	B,NPASS

MOV	A,B

CMA

OUT	STATL

PROGR2:	PUSH	B

LXI	D,BEGDAT

LHLD	BEGPRM

PROGR3:	LDAX	D

MOV	M,A

INX	D

INX	H

LDA	ENDPRM+1

CMP	H

JNZ	PROGR3

POP	B		;GET PASS COUNT

DCX	B

MOV	A,C		;DSIPLAY COUNT ON STATUS LIGHTS

CMA

OUT	STATL

MOV	A,B		;CHECK FOR PASSES = 0

ORA	C

JNZ	PROGR2		;LOOP IF NOT LAST PASS

LXI	D,OFFMSG

CALL	PRTMSG

PROGR5:	CALL	INCH

CPI	CR

JNZ	PROGR5

RET

;

;COMPARE ROUTINE TO COMPARE PROM'S TO MEMORY

;

COMPAR:	LDA	FUNCT

CPI	'E'

RZ

LXI	D,BEGDAT

LHLD	BEGPRM

COMPA1:	LDAX	D

CMP	M

JNZ	COMPA2

INX	H

INX	D

LDA	ENDPRM+1

CMP	H

JNZ	COMPA1

LXI	D,OKMSG

JMP	PRTMSG

COMPA2	LXI	D,BADMSG

;

;ROUTINE TO PRINT MESSAGE TERMINATED BY $ ON CONSOLE

;

PRTMSG:	MVI	C,WCONB		;PRINT MESSAGE ON CONSOLE

JMP	BDOS

;

;CHARACTER INPUT ROUTINE

;

INCH:	PUSH	B

PUSH	D

PUSH	H

MVI	C,RCON

CALL	BDOS

POP	H

POP	D

POP	B

RET

;

;CONSOLE MESSAGES

;

SGNMSG:	DB	CR,LF,CR,LF

DB	'CROMEMCO BYTESAVER 2708 EPROM PROGRAMMER'

DB	CR,LF,'RELEASE 1.4',CR,LF,'$'

FUNCMSG:DB	CR,LF,'SELECT OPTIONS:',CR,LF,CR,LF

DB	'     E - VERIFY ERASED',CR,LF

DB	'     C - COMPARE TO CONTENTS OF 1000H',CR,LF

DB	'     P - PROGRAM TO CONTENTS OF 1000H',CR,LF

DB	'     D - EXIT TO DDT',CR,LF

DB	'     X - EXIT TO CP/M',CR,LF,CR,LF,':$'

WHATMSG:DB	CR,LF,CR,LF,'THAT WASN''T ONE OF THE'

DB	' CHOICES !!!',CR,LF,CR,LF,'TRY AGAIN'

DB	CR,LF,':$'

RNGMSG1:DB	CR,LF,'EPROM SOCKET POSITION (0 - 7)',CR,LF

DB	'FIRST? ','$'

RNGMSG2:DB	CR,LF,'LAST ? ','$'

PRMMSG:	DB	CR,LF,CR,LF,'RANGE INVALID; MUST BE BETWEEN'

DB	' 0 - 7,'

DB	CR,LF,'AND END MUST BE > BEGINNING. TRY AGAIN.'

DB	CR,LF,'$'

ERMSG:	DB	CR,LF,CR,LF

DB	'EPROMS ARE ERASED.',CR,LF,'$'

NERMSG:	DB	CR,LF,CR,LF

DB	'EPROMS NOT ERASED !',CR,LF,'$'

PWRMSG:	DB	CR,LF

DB	'TURN PROGRAM POWER ON',CR,LF

DB	'TYPE CR TO CONTINUE ','$'

PGMMSG:	DB	CR,LF,CR,LF

DB	'PROGRAMMING NOW IN PROGRESS',CR,LF

DB	'PLEASE WAIT 2 MINUTES PER EPROM'

DB	CR,LF,CR,LF,'$'

OFFMSG:	DB	'PROGRAMMING COMPLETE',CR,LF

DB	'TURN PROGRAM POWER OFF',CR,LF

DB	'TYPE CR TO CONTINUE',CR,LF,'$'

OKMSG:	DB	CR,LF,CR,LF,'EPROMS CORRECTLY PROGRAMMED'

DB	CR,LF,'$'

BADMSG:	DB	CR,LF,CR,LF,'EPROM COMPARE ERROR!',CR,LF,'$'

;

;STORAGE ALLOCATIONS

;

BEGPRM:	DS	2		;EPROM START ADDRESS

ENDPRM:	DS	2		;EPROM END ADDRESS

FUNCT:	DS	1		;SELECTED FUNCTION

DS	40H		;PROGRAM STACK AREA

STACK:	EQU	$

END

___________________________________