If you want to try and download these programs to your Sol, here's how to do it.

- Grab the *.ent file you are interested from one of the tables below.

- Connect a serial cable from your PC to your Sol

- Set the baud rate, data bits, parity bits, and stop bits the same on the two machines.  I have difficulty getting my Sol to transfer reliably if the baud rate is higher than 1200.  YMMV.

- Test that the link works.  Use the TERM command to do so.

- On the Sol, type "SET I=1".  This makes it accept subsequent input from the serial port, as if you were entering it from the keyboard.

- On the PC, transfer the *.ent file over the serial link as a straight ASCII file.

- To run the program, type "EX xxxx", where xxxx is the load address, and off she goes!

If you have a better way of doing it, let me know!