NEW PRODUCT ANNOUNCEMENT

SOL-20 Keyboard Modification Kit

Barry Watzman is pleased to announce the availability of the model CKB-1 keyboard modification kit for the Processor Technology SOL-20 series micro-computer.  This kit modifies the 8-bit output from the numeric pad on the SOL-20 to produce an output with the high order bit (80H) true, allowing keys on the numeric pad to be distinguished from all other keys on the keyboard.  Included with the kit is an assortment of over two dozen double shot molded custom keytops with text-editing/ word-processing legends which match exactly in color and style the standard keytops supplied with the SOL-20.  Thus by installing this kit and making the appropriate software modifications, a user of ALS-8, The Electric Pencil or similar programs may now have explicit, clearly labeled keys for such functions as insert and delete line, insert and delete character, roll up, roll down, etc., rather than having to remember one or two dozen obscure control code sequences.

The model CKB-1 consists of the set of custom keytops, a special custom programmed ROM and instructions, and is installed simply by replacing U18 on the keyboard with the custom ROM supplied, replacing the numeric keytops with the  desired function keytops, and making the necessary changes in the user's software to recognize the new control codes (suggested patches for ALS-8 and the CP/M version of The Electric Pencil II are included).  And, since the only changes are to the 80H bit, the keyboard may be reverted to it's numeric mode either by re-installing the original IC ROM, or more simply, by doing an ANI 7FH in software.

The model CKB-1 sells for $24.95 and is available from:

Barry A. Watzman

Dept. LBA

560 Sunset Rd.

Benton Harbor, Mich. 49022